Annex 3 – Horizontal Accuracy Computation

T-0027

The Horizontal Accuracy Statement reported in Section F (Analysis of Results) is based on the predicted circular horizontal accuracy of adjusted points in the aerotriangulation solution.  This circular accuracy equals the radius of the 95% confidence circle as calculated from the horizontal (x and y) root-mean-square (RMS) values of the standard deviations for each triangulated ground point, rounded to the nearest tenth of a meter.

The root mean square of all standard deviations of triangulated ground points:

RMS(x)=0.095 meters	RMS(y)=0.150 meters

The value for the confidence circle radius is given by the following expression:

R=K*Sx

Where Sx is defined as the larger of the two (X and Y) RMS values, and K is interpolated using the C ratio from the Table of Cumulative Probability.

The C ratio equals the smaller of the RMS values divided by the larger:

C=0.095/0.150=0.633

The following line (95% probability level) from the Table of Cumulative Probability was used to determine the value of K by a simple linear interpolation between the two nearest values of C:

C	0	.1	.2	.3	.4	.5	.6	.7	.8	.9	1.0

K(95%)	1.95996	1.96253	1.97041	1.98420	2.00514	2.03586	2.08130	2.14598	2.23029	2.33180	2.44775

K	=2.08130+[(0.633-0.6/(0.7-0.6)*(2.14598-2.08130)]

=2.08130+(0.330*0.06468)

=2.08130+0.021344= 2.102644

K	=2.103

R=K*Sx=2.103*0.150=0.31545

The Radius of the 95% Confidence Circle=0.32 meters